## Slide 1
SEMICONDUCTOR TOOLING ALGORITHMS
Drift-Sense
Navigation-Error Recovery & Sub-Pixel Alignment for Wafer Inspection Tools
PROJECT CORE DELIVERABLES & TEAM ROLES
• Krish Deshpande (Algorithmic Lead): Preprocessing (CLAHE), Pyramidal Multi-Scale Search, NMS Peak Extraction, Periodicity Tie-Breaking, Sub- Pixel Parabolic Fitting, ORB+RANSAC AI Fallback, and Technical Documentation.
• Shubh Garg (Data & Evaluation): Synthetic Ground-Truth Data Pipeline, Metrics CSV Generation, Visualization Overlays & Repository Setup.

## Slide 2
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
Industry Challenge: Stage Drift in Wafer Inspection
1. Mechanical Drift
• Stage Hysteresis: Nanometer-scale mechanical vibration & stage motor drift.
• Thermal Shifts: Temperature fluctuations cause micro-shifts across optical fields.
• Position Drift: Optical tool fails to land at exact nominal site coordinates.
2. Optical Ambiguity
• High Periodicity: Semiconductor memory dies contain thousands of identical cell structures.
• Low Contrast: Silicon oxide/nitride layers produce low optical contrast.
• Illumination Noise: Sensor gain differences and dark currents degrade standard matchers.
3. Technical Solution
• Drift-Sense Engine: Deterministic, sub-pixel matching algorithm requiring 0ms training time.
• Nanometer Precision: Sub-0.03 pixel localization accuracy (~15 nm physical resolution).
• Scale Resilient: Pyramidal search handles ±15% optical magnification shifts.

## Slide 3
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
System Architecture & Processing Pipeline
STEP 1: PREPROCESS
• Input Capture: Search S (512x512) & Ref R (320x320)
• Adaptive CLAHE: Histogram equalization over 8x8 tiles
• Gaussian Blur: High-frequency noise reduction
• Sobel Edges: Gradient magnitude extraction
STEP 2: MULTI-SCALE
• Pyramidal Search: Scale range: s in [0.85, 1.15]
• Bicubic Scaling: High-quality template interpolation
• NCC Map: Normalized Cross-Correlation evaluation
• Response Tensor: Multi-resolution correlation space
STEP 3: NMS & TIE-BREAK
• NMS Filtering: Local dilation filter extracts top-K peaks
• Periodicity Check: Identifies competing grid peaks
• Stage Prior: Center distance penalty score
• High-Res Rescore: Pixel difference verification
STEP 4: SUB-PIXEL & AI
• 2D Parabola Fit: Sub-pixel parabolic quadratic curve fit
• Fractional Offset: Returns dx, dy sub-pixel shifts
• AI Fallback: ORB Keypoints + RANSAC Homography
• Final Output: Precise (x, y) & Confidence score

## Slide 4
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
Krish Deshpande : Algorithmic Core: Preprocessing & Pyramids
Adaptive Intensity Preprocessing (src/preprocess.py)
• CLAHE Contrast Equalization: Enhances local contrast in low-reflectance silicon oxide/metal layers without blowing out highlights.
• Gaussian Denoising (3x3): Attenuates high-frequency optical sensor shot noise.
• Sobel Gradient Magnitude: Extracts spatial edge structures to ensure robust matching even under non-linear lighting variation.
• Z-Score Calibration: Normalizes intensity variations for zero mean and unit variance.
Pyramidal Multi-Scale Search Space (src/matcher.py)
• Scale Invariance: Evaluates template scale hypotheses across s in {s_base * 0.95, s_base, s_base * 1.05}.
• Bicubic & Area Resampling: Uses INTER_AREA for downscaling and INTER_CUBIC for upscaling to prevent aliasing.
• Normalized Cross-Correlation (NCC): Computes scale-normalized inner product invariant to linear gain shifts.
• 0ms Training Latency: Fully deterministic signal processing engine with zero GPU training overhead.

## Slide 5
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
Periodicity Tie-Breaking & Sub-Pixel Parabolic Fit
Periodicity & Stage Prior Tie-Breaking (src/peaks.py)
• Non-Maximum Suppression (NMS): Extracts local peak candidates using 2D dilation morphology.
• Grid Ambiguity Detection: Detects when multiple candidate peaks exhibit correlation within 5% of global maximum.
• Physical Stage Prior: Applies physical stage drift prior penalty favoring peaks closer to search ROI center.
• Composite Fitness Score: Fitness = 0.8 * NormScore + 0.2 * (1 - NormDistPenalty).
Sub-Pixel Quadratic Surface Fit (src/peaks.py)
• Discretization Limit: Camera sensor pixels discritize position into 1px steps (~500nm).
• 2D Parabolic Interpolation: Fits continuous quadratic surface through 3x3 correlation neighborhood around integer peak.
• Fractional Shift Equation: dx = (Left - Right) / (2 * (Left - 2*Center + Right)).
• Extreme Precision: Achieves nanometer-level spatial localization (< 0.03 px error).

## Slide 6
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
AI Feature Matching Fallback & Resilience
Zero-Shot AI Feature Matching Engine (ORB + RANSAC)
• Dynamic Trigger: Engages automatically when normalized cross-correlation confidence drops below 0.40 under extreme distortion.
• ORB Keypoint Extraction: Detects 1,000 scale-invariant oriented FAST keypoints and binary BRIEF descriptors.
• FLANN / Brute-Force Matcher: Computes Hamming distance between reference and search keypoint descriptors.
• RANSAC Homography Estimation: Filters geometric outliers using 4-point perspective RANSAC (threshold = 5.0 px).
• Perspective Projection: Transforms template center coordinate through homography matrix H to locate target with high confidence.

## Slide 7
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
Empirical Benchmark & Performance Verification
MEDIAN ERROR
• 0.029 px: Sub-15nm physical resolution
HIT RATE (< 1px)
• 100.0%: On unique wafer pattern sites
HIT RATE (< 5px)
• 80.0%: Overall across all 40 test cases
TRAINING LATENCY
• 0 ms: Deterministic zero-shot inference
Benchmark Execution Results Summary (data/synthetic/ground_truth.csv)
• Sample #000 (Easy Unique Pattern): True: (111.0, 221.0) | Pred: (110.9601, 221.0228) | Error: 0.046 px | Score: 0.8553
• Sample #015 (Easy Unique Pattern): True: (207.0, 373.0) | Pred: (207.0207, 373.0123) | Error: 0.024 px | Score: 0.8508
• Sample #036 (Hard Periodic Pattern): True: (432.0, 112.0) | Pred: (431.9930, 111.9910) | Error: 0.011 px | Score: 0.8548
• Overall Dataset Summary: 40 Test Cases | Median Error: 0.029 px | Average Match Confidence: 0.845

## Slide 8
DRIFT-SENSE / SEMICONDUCTOR ALGORITHMIC TOOLING
Conclusion & Future Hardware Roadmap
1. Production Ready
• High Accuracy: Median positioning error of 0.029 pixels.
• Sub-Pixel Resolution: Resolves sub-15nm displacement.
• Zero Training Cost: Instant deployment without model weights.
2. Robust Engineering
• Multi-Scale Pyramid: Handles magnification drift.
• Periodicity Prior: Resolves repeating memory arrays.
• AI Fallback: Recovers from heavy optical noise.
3. Future Acceleration
• FPGA / ASIC IP: Hardware-accelerated 2D NCC correlation pipeline.
• Sub-Graph Super-Res: Deep learning sub-pixel feature enhancement.
• Multi-Die Alignment: Simultaneous multi-ROI wafer alignment.